Lustre, ZFS, and Data Integrity
Lustre ZFS Team
Sun Microsystems
Andreas Dilger
Sr. Staff Engineer
Sun Microsystems
ZFS BOF Supercomputing 2009

---
Topics
Topics
Overview
ZFS/DMU features
ZFS Data Integrity
Lustre Data Integrity
ZFS-Lustre Integration
Current Status

---
HPCS Requirements
2012 Lustre Requirements
Filesystem Limits
  - 240 PB file system size
  - 1 trillion files (1012) per file system
  - 1.5 TB/s aggregate bandwidth
  - 100k clients
Single File/Directory Limits
  - 10 billion files in a single directory
  - 0 to 1 PB file size range
Reliability
  - 100h filesystem integrity check
  - End-to-end data integrity

---
ZFS
ZFS Meets Future Requirements
Capacity
  - Single filesystems 512TB+ (theoretical 264 devices * 264 bytes)
  - Trillions of files in a single file system (theoretical 248 files per fileset)
  - Dynamic addition of capacity/performance
Reliability and Integrity
  - Transaction based, copy-on-write
  - Internal data redundancy (up to triple parity/mirror and/or 3 copies)
  - End-to-end checksum of all data/metadata
  - Online integrity verification and reconstruction
Functionality
  - Snapshots, filesets, compression, encryption
  - Online incremental backup/restore
  - Hybrid storage pools (HDD + SSD)
  - Portable code base (BSD, Solaris, ... Linux, OS/X?)

---
Lustre/ZFS Project Background
ZFS-FUSE (2006)
The first project of ZFS porting to the FUSE framework for the Linux in the user space
Kernel DMU (2008)
LLNL engineer ported core parts of ZFS to RedHat Linux as a kernel module
Lustre-kDMU (2008 – present)
Modify Lustre to work on ZFS/DMU storage backend for a production environment
ZFS BOF Supercomputing 2009

---
ZFS Overview
ZFS POSIX Layer (ZPL)
- Interface to user applications
- Directories, namespace, ACLs, xattr
Data Management Unit (DMU)
- Objects, datatsets, snapshots
- Copy-on-write atomic transactions
- name->value lookup tables (ZAP)
Adaptive Replacement Cache (ARC)
Manage RAM, flash cache space
Storage Pool Allocator (SPA)
- Allocate blocks at IO time
- Manages multiple disks directly
- Mirroring, parity, compression
ZFS BOF Supercomputing 2009

---
Lustre/Kernel DMU Modules
ZFS BOF Supercomputing 2009

---
Lustre Software Stack Updates
1.8/2.0 OSS
1.8 MDS
2.0 MDS
2.1 MDS
2.1 OSS
MDT
OST
MDT
 MDT
OST
MDS
obdfilter
MDD
MDD
OFD
fsfilt
fsfilt
ldiskfs
 OSD
DMU
OSD
DMU
OSD
ldiskfs
ldiskfs
ldiskfs
DMU
DMU
ZFS BOF Supercomputing 2009

---
Data Integrity in Communications
How Safe Is Your Data?
- There are many sources of data corruption
  - Software/firmware: client, NIC, router, server, HBA, disk
  - RAM, CPU, disk cache, media
  - Client network, storage network, cables
Object Storage Server
Client
Storage
Application
Server
Router
Transport
Transport
Network
Network
Network
Link
Link
Link

---
ZFS End-to-end Data Integrity
ZFS Industry Leading Data Integrity

---
End-to-End Data Integrity
End-to-End Data Integrity
Lustre Network Checksum
  - Detects data corruption over network
  - Ext3/4 does not checksum data on disk
ZFS stores data/metadata checksums
  - Fast (Fletcher-4 default, or none)
  - Strong (SHA-256)
Combine for End-to-End Integrity
  - Integrate Lustre and ZFS checksums
  - Avoid recompute full checksum on data
  - Always overlap checksum coverage
  - Use scalable tree hash method

---
Hash Tree and Multiple Block Sizes

---
End-to-End Integrity Client Write

---
End-to-End Integrity Server Write

---
Integrity Checking Targets
Scale of proposed filesystem is enormous
  - 1 trillion files checked in 100h
  - 2-4PB of MDT filesystem metadata
  - ~3 million files/sec, 3GB/s+ for one pass
Need to handle CMD coherency as well
  - Distributed link count on files, directories
  - Directory parent/child relationship
  - Filename to FID to inode mapping

---
Distributed Coherency Checking
Traverse MDT filesystem(s) only once
  - Piggyback on ZFS resilver/scrub to avoid extra IO
  - Lustre processes blocks after checksum validation
Validate OST/remote MDT data opportunistically
  - Track which objects have not been validated (1 bit/object)
  - Each object has a back-reference to validate user
  - Back-reference avoids need to keep global reference table
Lazily scan OST/MDT in the background
  - Load sensitive scanning
  - Continuous online verification/fix of distributed state

---
Lustre DMU development Status
Data Alpha
  - OST basic functionality
MD Alpha
  - MDS basic functionality, beginning recovery support
Beta
  - Layouts, performance improvement, full recovery
GA
  - Full performance in production release
ZFS BOF Supercomputing 2009

---
Thank You
Questions?
ZFS BOF Supercomputing 2009

---
Hash Tree For Non-contiguous Data
ZFS BOF Supercomputing 2009

---
       T10-DIF vs. Hash Tree
Fletcher-4 Checksum
  - All 1- 2- 3- 4-bit errors
  - All errors affecting 4 or fewer 32-bit words
  - Single 128-bit burst error
  - 10-13 bit error rate
Hash Tree
  - Misplaced read
  - Misplaced write
  - Phantom write
  - Bad RAID reconstruction
CRC-16 Guard Word
  - All 1-bit errors
  - All adjacent 2-bit errors
  - Single 16-bit burst error
  - 10-5 bit error rate
32-bit Reference Tag
  - Misplaced write != 2nTB
  - Misplaced read != 2nTB

---
ZFS Hybrid Pool Example
4 Xeon 7350 Processors (16 cores)
32GB FB DDR2 ECC DRAM
OpenSolarisTM with ZFS
Configuration B
Configuration A
Seven 146GB 10,000 RPM SAS Drives
Five 400GB 4200 RPM SATA Drives
32GB SSD ZIL Device
80GB SSD Cache Device

---
ZFS Hybrid Pool Example
3.2x
2x
1.1x
1/5
Raw Capacity (2TB)
Power
Read IOPs
Write IOPs
Hybrid Storage(DRAM + SSD + 5x 4200 SATA)
Traditional Storage (DRAM + 7x 10K SAS)

---
Lustre kDMU Roadmap